## Slide 1: Introduction to SCARES Mesh NETWORK
For
SCARES
South County Amateur Radio Emergency Service
Amateur Radio EMCOMM
Gary Aden, K6GDA
Nov 19, 2015

## Slide 2: Outline
What is a Mesh network
What is a MESH node?
Advantages of Mesh Networks
MESH and Amateur Radio
Hardware
Software
The SCARES MESH

## Slide 3: What is a MESH Network?
A MESH network is a group of MESH nodes that wirelessly communicate with each other

## Slide 4: What is a MESH Network?
If one MESH node drops the remainder of the MESH can still function

## Slide 5: What is a MESH Network?
If the MESH node is restored then the net is self discovering and…

## Slide 6: What is a MESH Network?
If the MESH node is restored then the net is self discovering and…self healing

## Slide 7: What is a MESH Node?
• Each node…
  Is a radio transmitter/receiver with router…
  builds a routing table that tracks the other nodes…
  will pass data from one to the next until the final connection is made.... completely automatically …
  can be remotely managed, you do not need physical access once installed.
• If any node is connected to resources it can provide access to the entire network.
  internet, video camera, fileserver, mail server, etc.

## Slide 8: Advantages of a MESH Network
Does not use or rely on the internet
Does not use or rely on cell towers
Is relatively inexpensive to implement (~ $200/node)
Is self forming and self healing
Can still operates even if part of the mesh network goes down
Has a very low power requirement
Supports relatively high demand
Can pass written text and pictures

## Slide 9: MESH and Amateur Radio
802.11g Wireless Band

## Slide 10: Hardware - Ubiquity
Ubiquiti 2.4GHz (13 cm band)
Pico M2, $79
Bullet M2 HP, $76 + antenna
AirGrid M2 HP, $69
NanoStation Loco M2, $69
NanoStation M2, $79
Rocket M2, $79 + antenna

## Slide 11: Software - AREDN
AMATEUR RADIO EMERGENCY DATA NETWORK
AREDN Project software
  written for MESH emergency data network
  a new method of providing high-speed data
  uses in the amateur radio frequencies
It comes in part from the developers of Broadband Hamnet which was formerly known as HSMM-MESH.

## Slide 12: MESH – Can You Connect?

## Slide 13: Typical MESH Status

## Slide 14: MESH Status (SCARES Nov 2015)

## Slide 15: MESH-What’s Next?
Get more SCARES nodes active
Get more EOC’s connected
Start connecting CERT trailers
Set up a protocol for using a MESH in an emergency
Start practicing using MESH along with Voice
Set up Demo’s for the cities and county SCARES serves

## Slide 16: MESH
Thank you