## Slide 1: Repeaters, Remote Bases, Simplex
By
Robert (Bob) Lombaerde, WB6WGM
South County ARES
21 Nov 2024

## Slide 2: Presentation Outline
Introduction
What is a repeater?
What is a Remote Base?
SCARES repeaters
Repeater diagram details
Nuances
Propagation
Questions

## Slide 3: Repeater: Receives on Frequency 1 Transmits Simultaneously on Frequency 2

## Slide 4: SCARES repeaters
Number of SCARES repeaters - 3
Frequencies 444.5+ MHz PL 100 Hz 53.68- MHz PL 114.8 Hz
Locations Hall of Justice RWC (primary 444.5) RWC PD (aux repeater 444.5) Kings Mountain Fire Station (53.68)

## Slide 5: What the repeater user needs to know
Repeater’s output frequency
Repeater’s input frequency (or offset)
CTCSS required to access the repeater?
Does repeater transmit CTCSS?
Is it an OPEN repeater?

## Slide 6: NARCC
Northern Amateur Relay Council of California

## Slide 7: Repeater offset on radio
Receive Frequency 444.5
Transmit Frequency 449.5 (+5)
PTT
RTL

## Slide 8: SCARES auxiliary repeater
Located in RWCPD Ham radio room
On “hot standby”
Battery backup w/trickle charge
No Remote Base
Commanded ON if HoJ repeater is down
Available as portable ? (not easy,heavy)

## Slide 9: SCARES repeater in RWCPD
Duplexer
Yaesu Vertex VXR-5000 25 W UHF repeater
Pacific Research controller plugged-in
Diamond X-50A
UHF
Antenna
TX 444.5
RX 449.5

## Slide 10: SCARES aux repeater

## Slide 11: SCARES aux repeater

## Slide 12: SCARES 6 m repeater
GE mobile transceiver configured as a repeater, 53.68- PL 114.8
Pacific Research Controller
No remote base
Battery backed up by KMF
Utilizes KMF 6m folded dipole antenna
SCARES 53.68 duplexer

## Slide 13: SCARES 6 meter repeater before KM install

## Slide 14: 6 meter repeater at KM Fire

## Slide 15: SCARES primary UHF repeater
Located atop the Hall of Justice in RWC
25 W Kenwood UHF repeater with DSP
100 Hz CTCSS both TX/RX
DB-408 dipole antenna configured for maximum gain along peninsula
Three channel Arcom RC210 controller
Kenwood 2 meter remote base

## Slide 16: Remote Base ?
Remotely Controlled Base Station
A mobile 2m Kenwood TM-281 @25 W
Think of it as a base radio but located at another site (at the repeater)
Controlled by the repeater’s ARCOM controller

## Slide 17: K6MPN primary Repeater (front – back)

## Slide 18: VHF and UHF antennas

## Slide 19: SCARES Repeater on HoJ
Arcom
RC210
Controller
Duplexer
Kenwood UHF repeater
2m xceiver
filter
DB-222
VHF Antenna
DB-408
UHF
Antenna
TX 444.5
RX 449.5
UPS
DC power supply
PolyPhasers

## Slide 20: Repeater Controller (basic)
Processes audio from the receiver
Sends processed audio to transmitter
Keys the transmitter
Inserts repeater ID (10 minute interval)
Has watchdog timer (shuts off TX if TX stuck ON or someone has “talked off” the repeater) 90 sec tx timer limit

## Slide 21: SCARES repeater nuances
Announces net 5 minutes after the hour on Mondays from 0800 to 1900 hrs.
Announces general meeting 5 minutes after the hour every third Thursday from 0800 to 1900 hrs.
Turns ON remote base 1915 hrs every Monday for net and then turns remote base OFF at 2015 hrs.

## Slide 22: SCARES repeater nuances-2
90 second time-out-timer
Short hang-time for Remote Base
Voice ID switches to CW if people are talking on the repeater
Remote Base is steerable
Automatically adjusts for DST/PST

## Slide 23: SCARES repeater nuances-3
Don’t transmit during RB activation
During nets when RB is ON, 2m input will trigger a triple beep
Don’t announce you will be out of town

## Slide 24: Simplex Repeaters
“Simplex Repeater” is NOT a repeater
Not simultaneous transmission of voice
Acts like a parrot – repeating input
Should be monitored/controlled by user
Useful for extending range of comms for a group
Not suitable for 24/7 operation
Can be used outside of repeater bands

## Slide 25: Connecting to the world digitally via VOIP, internet
D-Star – Icom, Kenwood
Fusion, Yaesu
IRLC/ECHOlink
DMR, Digital Mobile Radio
APCO P25
Can SCARES repeater use VOIP/internet?
No – no internet and no phone line

## Slide 26: Wires (Yaesu)
Yaesu DTMF encode option
Allows access to repeater connected to internet for world wide access
Sends out DTMF code to open gateway
Blanks out speech during first part of transmission. You only hear “---WGM”
Unfortunately easily turned ON – causing loss of voice initially

## Slide 27: NARCC
Northern Amateur Relay Council of California

## Slide 28: NARCC (cont.) showing open/closed and Fusion,DMR

## Slide 29: Simplex
SCARES “in the old days, before the repeater” Nets were 2m simplex
With height, long line-of-sight distances are possible - SOTA
Relays were used so all could check-in
Locally omni antennas worked well, for distance directional antenna are better
W6VOM, Neil in Dublin, K6VP, Dan, SJ

## Slide 30: Multi-path - reflections

## Slide 31: Multipath problems
Multiple delayed signals received
Caused by reflections due to – hills, walls, buildings, atmosphere, etc
Causes distortion in receiver
Cured by receiving best signal with directional antenna

## Slide 32: Repeaters, Simplex, etc.
Questions ??